## Slide 1: PPM Images
CPSC 1020

## Slide 2: Overview
Stands for Portable Pixel Map
They have a simple format
You will need a specific viewer to view ppm
Gimp works for Windows, Mac, or Linux (little slow)
IrfanView (www.irfanview.com) works for windows as well
lab computers - on terminal use the command display
Images contain two important things
  header
  group of pixels
    each pixel has three values RGB (red, green, and blue)

## Slide 3: PPM headers

## Slide 4: examples of headers
P6 1024 788 255
or
P6
400 400 255
or
P6
#This is a comment
400 400 #This is another comment
255
You can add comments using #comment

## Slide 5
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Header
Binary data
P6: tells the computer it is a ppm file
2: tells the computer the width (columns) of the image is 2 pixels
3: tells the computer the height (rows) of the image is 3 pixels
255: tells the computer the maximum color value (this is always 255)
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
3 rows
2 columns

## Slide 6
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Header
Binary data
P6: tells the computer it is a ppm file
2: tells the computer the width (columns) of the image is 2 pixels
3: tells the computer the height (rows) of the image is 3 pixels
255: tells the computer the maximum color value (this is always 255)
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
3 rows
2 columns
The remainder of the file is binary data

## Slide 7
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Header
Binary data
P6: tells the computer it is a ppm file
2: tells the computer the width (columns) of the image is 2 pixels
3: tells the computer the height (rows) of the image is 3 pixels
255: tells the computer the maximum color value (this is always 255)
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
3 rows
2 columns
Conceptually, you can think of the binary data as a consecutive set of bytes
Each set of three bytes represents a pixel
Each pixel represents a color channel (RGB)

## Slide 8
If I were to "decode", each set of three would represent a pixel, with the bytes in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
2 columns
3 rows

## Slide 9
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
2 columns
3 rows
0 red, 0 green, 0 blue = black

## Slide 10
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
 | 0 | 1
0 |  | 
1 |  | 
2 |  | 
2 columns
3 rows
255 red, 255 green, 0 blue = yellow
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255

## Slide 11
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
 | 0 | 1
0 |  | 
1 |  | 
2 columns
3 rows
255 red, 0 green, 0 blue = red

## Slide 12
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
 | 0 | 1
0 |  | 
1 |  | 
2 columns
3 rows
0 red, 0 green, 255 blue = blue

## Slide 13
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
 | 0 | 1
0 |  | 
1 |  | 
2 columns
3 rows
0 red, 255 green, 0 blue = green

## Slide 14
P6
2 3 255
0 0 0 255 255 0
255 0 0 0 0 255
0 255 0 255 255 255
Each set of three after that determines the color of a pixel in this order:
Amount red (0-255)
Amount green (0-255)
Amount blue (0-255)
 | 0 | 1
0 |  | 
1 |  | 
2 columns
3 rows
255 red, 255 green, 255 blue = white

## Slide 15: Let’s look at some code
We will look at a couple quick program
How many bytes does it take to create a 400 X 400 image?
convert ppm to jpg
in terminal type:
convert filename.ppm filename.jpg