## Slide 1: CPSC3300: Computer Systems Organization
Lectures 9 & 10 – MIPS Instructions & Datapath

## Slide 2: Overview
Elements in the datapath
  Program counter (PC)
  Instruction memory
  ALU
  Register file
  Data memory
Datapath for various instructions
Reading
  Chp4.1-3
  Reading: RISC vs. CISC
  https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/
  MIPS vs ARM
  http://www.differencebetween.com/difference-between-mips-and-vs-arm/

## Slide 3: Instruction and Data Memories
Cache memory
  SRAM device
  faster
  Low capacity
  Expensive
  Inside processor chip
Used as cache to hold instructions and data likely to be reused
instruction memory holds instruction
data memory holds data
Main memory
  DRAM device
  slower
  High capacity
  Cheaper
  Outside processor chip
Used as main memory

## Slide 4: RISC vs CISC
RISC: reduced instruction set computing
  Register-register type
  Fixed instruction size
  MIPS, ARM, SPARC, mostly appearing in smart phones, tablet computers
  reading: Difference between MIPS and ARM http://www.differencebetween.com/difference-between-mips-and-vs-arm/
CISC: complex instruction set computing
  X86, x86_64
  Reading: RISC vs. CISC https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 5: 3 Types of MIPS Instructions
  R type: read two registers, write one register
    Arithmetic computation
      Addition
      add $rd, $rs1, $rs2 #$rd  $rs1 + $rs2
    Logical computation
      And
      and $rd, $rs1, $rs2 #$rd  $rs1 & $rs2
  J type: no register operand
    Jump to an address

## Slide 6: 3 Types of MIPS Instructions
I type: two register operands
  Arithmetic computation with immediates (constants)
    Read one register, write one register, e.g.,
    add $rt, $rs, 10 #$rt  $rs + 10
  Branch: if-else, for, while, switch
    Read two registers, e.g,
    beq $t0, $t1, Target #branch to Target if $t0 == $t1
  Load data from memory or store data to memory
    Load: read one register, write one register, i.e.,
    lw $8, 12($16) # $8  mem($16+12)
    Store: read two registers
    sw $8, 12($16) # $8  mem($16+12)

## Slide 7: 32-bit MIPS Instructions
3 types of instructions, each instruction 32 bits
A total of 32 registers, 5-bit register address
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store I-type
Branch I-type
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 8: Instruction Execution on Processors
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 9: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
We focus on single-cycle design, which finishes all steps in a single clock cycle

## Slide 10: Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 11: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 12: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset (constant)
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 13: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 14: Target Addressing Example
Loop code from earlier example
  Assume Loop at location (80000)10
Loop: sll $9, $19, 2 | 80000 | 0 | 0 | 19 | 9 | 2 | 0
add $9, $9, $22 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $8, 0($9) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $8, $21, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $19, $19, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 
bne instruction corresponds to a PC value of 80012,
Exit label corresponds to a PC value of 80024,
2x word length (2*4) added to PC value of next instruction (PC+4) when branch taken:
Next instruction: PC+4 (80016), 8 is added and instruction after Exit label will run next

## Slide 15: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 16: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 17: Single-cycle Instruction execution
R-type
  Fetch instruction and increment PC
  Read two source registers from register file (set control)
  Perform ALU operation on register operands
  Write ALU result back to register
Store/Load
  Fetch instruction and increment PC
  Read one register value from register file (set control)
  ALU computes sum of immediate and register value
  ALU result used as address to memory
  Data from memory written back to register (Load only)
Branch
  Fetch instruction and increment PC
  Read two source registers from register file (set control)
  ALU performs subtract on register operands (target addr computed)
  Zero result from ALU determines PC

## Slide 18: R-Type/Load/Store Datapath

## Slide 19: Full Datapath

## Slide 20: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 21: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 22: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 23: Datapath With Control

## Slide 24: R-Type Instruction

## Slide 25: Load Instruction

## Slide 26: Branch-on-Equal Instruction

## Slide 27: Implementing Jumps
Jump uses word address
Need an extra control signal decoded from opcode
Direct jump addressing
  PC: the address of the instruction following the jump
  Full target address = PC31…28 : (address × 4)
2
address
31:26
25:0
Jump
Why can we concatenate 00 to the address?
PC31…28
Address
00
4bits
26bits
2bits

## Slide 28: Datapath With Jumps Added

## Slide 29: Performance Issues of Single Cycle Datapath
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 30: Summary
Elements in datapath
Datapath for R, I, and J types of MIPS32
Control for MIPS32