## Slide 1: CPSC3300: Computer Systems Organization
Lecture 11 – Pipeline Datapath

## Slide 2: Administrivia
Project 1
  Due February 26
HW3
  Available online, due Tuesday March 9
Reading
  Chp 4.4-6

## Slide 3: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages

## Slide 4: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 5: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 6: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 7: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionsnonpipelined
  Time between instructionspipelined
  = Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 8: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 9: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 10: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 11: State of pipeline in a given cycle

## Slide 12: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 13: Pipeline Data Hazard Types
Pipeline hazard occurs when dependence exists and instr’s are close enough that instr overlap changes operand access order
Named by “ordering that must be preserved”
Types of data hazards (i followed by j)
  Read After Write (RAW) (aka true dependence)
    j tries to read operand before i writes it
  Write After Read (WAR) (Antidependence, a)
    j tries to write operand before i reads it
  Write After Write (WAW) (Output dependence, o)
    j tries to write operand before i writes it
  Read After Read (RAR) (Input dependence, i)
    i and j read the value of some variable

## Slide 14: RAW
RAW hazard: later instruction tries to read an operand before earlier instruction writes it
The dependence
add R1, R2, R3
sub R5, R1, R4
The hazard
IF | ID | EX | MEM | WB
IF | ID | EX | MEM | WB

## Slide 15: WAW
WAW hazard: later instruction tries to write an operand before earlier instruction writes it
The dependence
add R1, R2, R3
sub R1, R2, R4
The hazard
WAW hazard possible in a reasonable pipeline, but not in the very simple pipeline we are assuming
IF | ID | EX | MEM1 | MEM2 | MEM3 | WB
IF | ID | EX | MEM | WB

## Slide 16: Interlocks
When threatened by a hazard
Stall (pause a part of the pipeline by inserting no-op)
  Stalling avoids overlap that would cause error
  Stalling slows things down
Add hardware to avoid the hazards
  Details of hardware depend on hazard and pipeline

## Slide 17: Data Dependence Graph
Main data structure: dependence DAG
Nodes represent instructions
Edges (s1,s2) represent dependences between instructions
  Instruction s1 must execute before s2
Sometimes called data-flow graph

## Slide 18: Dependence Graph Example
Sample code
  sub $2, $1,$3
  and $12,$2,$5
  or $13,$6,$2
  add $14,$2,$2
  sw $15,100($2)
1
3
2
4
5
RAW
RAW
RAW
RAW

## Slide 19: Dependence Graph Example
Sample code
  sub $2, $1,$3
  and $12,$2,$5
  or $12,$6,$2
  add $6,$2,$2
  sw $15,100($2)
1
3
2
4
5
2/RAW
2/RAW
2/RAW
2/RAW
6/WAR
12/WAW

## Slide 20: Data Dependence Graph Example
S1 ADD R1, R2, R3
S2 BEQZ R1, L1
S3 ADD R4, R2, R5
S4 ADDI R5, R4, 1
S5 L1:ADDI R4, R5, 2
i
o
a
i
a
Data Dependence Graph
S3
R1/RAW
S1
S2
S5
o
S4
a
i
a
i
R4/RAW
R5/RAW

## Slide 21: Summary
MIPS pipeline
Single cycle graph
Pipeline multiple cycle graph
Data dependence and data dependence graph