## Slide 1: CPSC3300: Computer Systems Organization
Lecture 12 – Pipeline Hazards

## Slide 2: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 3: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
  DAG is used to identify data dependencies
Control hazard
  Deciding on control action depends on previous instruction

## Slide 4: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 5: Structure Hazard
In addition to IM and DM, what other structures (hardware) are duplicated to resolve structure hazard?

## Slide 6: Data Hazards
An instruction depends on completion of data access by a previous instruction
  True dependence in MIPS: RAW
    add $s0, $t0, $t1 sub $t2, $s0, $t3
Simple solution:
  stall the pipeline by inserting NO-OP (0x00000000)
  Instruction exec. delayed, performance poor

## Slide 7: Forwarding (aka Bypassing)
Better solution: use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath
Extra connection

## Slide 8: Load-Use Data Hazard
Forwarding can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
If the previous instruction is lw, a bubble must be inserted in addition to forwarding
Forwarding +
stall

## Slide 9: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F; Operands in memory
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles
Whose job is it?
Compiler should do the scheduling, but it is increasingly implemented in hardware.

## Slide 10: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
We have learned
  Structure hazard: duplicated/separated hardware to resolve it
  Data hazard: detection by examining dependencies, and forwarding to reduce its impact
How about control hazard?

## Slide 11: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
    The following instruction may not be the one to be executed
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 12: Branch Hazards
If no special treatment on branch instruction,
  extra branch outcome determined in MEM
Flush these instructions
(Set control values to 0)
PC
7

## Slide 13: Stall on Branch
Special treatment: execute the target address by the end of the ID stage
Stall the pipeline until branch outcome determined before fetching next instruction
Target address is available after the ID stage
One No-Op inserted

## Slide 14: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
    Pipeline executes as normal if prediction is correct
  Fetch instruction after branch, with no delay

## Slide 15: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 16: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
More advanced branch prediction will be introduced next lecture
The BIG Picture
  Insights for programmers:
  Use branches wisely
  Order your instructions wisely