## Slide 1: CPSC3300: Computer Systems Organization
Lecture 13 – Branch Hazards and Branch Prediction & Floating-Point Pipeline

## Slide 2: Overview
Control hazard and penalty control
Pipeline supporting floating point numbers
Reading
  Chp 4.8

## Slide 3: What We Learned about Branches
Hardware to reduce branch penalty
  Move hardware to examine branch condition and calculate target address early
    Both finish at the ID stage of the branch instruction, instead of the EXE stage
Still, there is one instruction delay
  A bubble inserted after the branch instruction
How about situations that would cause bubbles before the branch instruction?
  Does the branch instruction have dependencies with previous instructions?

## Slide 4: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can resolve using forwarding
Data forwarding

## Slide 5: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target
Bubble inserted
This example shows what really happens in HW.
We usually draw with a bubble for five stages and IF moved down to align with the other 4 stages. The effect is equivalent.

## Slide 6: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw $1, addr
beq $1, $0, target
Bubbles inserted

## Slide 7: Reducing Branch Penalty
Branch penalty in dynamically scheduled processors: wasted cycles due to pipeline flushing on mis-predicted branches
Reduce branch penalty:
Predict branch/jump instructions AND branch direction (taken or not taken)
Predict branch/jump target address (for taken branches)
Speculatively execute instructions along the predicted path

## Slide 8: Branch Direction Prediction
Predict branch direction: taken or not taken (T/NT)
Static prediction
  Compiler-determined prediction
  Fixed for the life of the program
Dynamic prediction:
  The prediction changes as program behavior changes
  branch prediction implemented in hardware
  common algorithm based on branch history
    predict the branch taken if branched the last time
    predict the branch not-taken if didn’t branch the last time
Not taken
taken
BNE R1, R2, L1
…
L1: …

## Slide 9: A Single Prediction Bit
1-bit predictor has a low accuracy
1-bit prediction
1: predict T
0: predict NT
The prediction changes with the most recent program behavior
state
2. Predict
Output T/NT
1. Access
3. Feedback T/NT
PC
T
1
0
T
NT
NT
General form: finite state machine

## Slide 10: Weakness of a Single Prediction Bit
Consider a nested loop of 9 iterations before exit:
  For (){
  for (i=0; i<9; i++)
  a[i] = a[i] * 2.0;
  }
  How many mispredictions?
  2 times:
  End of loop case, when it exits instead of looping as before
  First time through loop on next time through code, when it predicts exit instead of looping
  Only 80% accuracy even if loop 90% of the time

## Slide 11: 2-bit Branch Prediction for Loops
Algorithm: have to be wrong twice before the prediction is changed
Blue: stop, not taken
Green: go, taken
Adds hysteresis to decision making process
T
T
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
11
10
01
00
T
NT
T
NT
NT

## Slide 12: Accuracy of Different Schemes (Figure 3.15, p. 206)
4096 Entries 2-bit BHT (Branch History Table)
Unlimited Entries 2-bit BHT
1024 Entries (2,2) BHT
Frequency of Mispredictions

## Slide 13: Conceptual view of FP pipeline
The pipeline is for INT
Suppose FP has same pipeline as INT
Two changes
  EX may be repeated
  Multiple EX FP units
Stalls
  structural or data hazards
  EX completion of multi-cycle op
Four non-piped functional units
  int load/store, ALU ops, branches
  FP and int multiply
  FP add, sub, conversion
  FP int, divide

## Slide 14: The Execution Pipeline (e.g. Pipelined Functional Units)
Latency
  number of intervening cycles between an instruction that produces a result and an instruction that uses the result. Ex:
    ALU reg1 op reg2 stored in EX (0);
    load reg1 loaded in MEM (1)
Initiation interval
  number cycles that must elapse between issuing two ops of a given type

## Slide 15: Multiple Outstanding Operations
Pipelined EX unit allows
  4 outstanding FP adds
  7 outstanding FP/int multiplies
  1 outstanding FP divide
stage names
Requires:
Additional temp regs

## Slide 16: Multi-cycle Example
RAW hazards
Stall even F2’s value available b.c. MEM
used for ADD
If stalled for MUL, stalled for later ins.
If stalled for ADD, stalled for later ins.

## Slide 17: Hazard Detection and Forwarding
Structural hazards
  For divides
  Multiple reg writes in single cycle can occur (single write port)
Data hazards
  Out of order (OOO) completion possible
    WAW hazards since WB occur OOO (L.D one cycle earlier + dest F2)
    Problems with exceptions
  RAW hazards more frequent due to long latency ops

## Slide 18: Implementing Hazard Detection and Forwarding
Multiple reg writes in single cycle can occur (single write port)
  Multiple write ports, not efficiently used
  Track use of write port and stall before issue (ID stage)
WAW hazards since WB occur OOO (out of order)
  Delay issue of load
  Stamp out result of add.d
Before instruction issue:
  Check for structural hazards
  Check for RAW hazards
  Check for WAW hazards
Conceptually the same to implement, yet more cumbersome

## Slide 19: Summary
Branch prediction
Static vs dynamic prediction
BHT (Branch history table)
  1-bit vs. 2-bit
Pipeline for FP operations