## Slide 1: CPSC3300: Computer Systems Organization
Lecture 2 – Technology, Performance and Power

## Slide 2: Administrivia
Homework 1
  To be assigned. Description available on Canvas January 14th
  Due Thursday, January 28 11:59pm on Canvas
Reading sections
  Chp1.4-6
  Zybooks participation activities for 1.1-1.3 due Jan. 19, participation activities for 1.4-1.5 assigned today, due Jan. 21
About late assignments
  For each day late there will be a 10% deduction
  No late homework assignment submissions accepted once the solution has been made available for that assignment

## Slide 3: Overview
Technology
  Moore’s law
CPU performance
  Elapsed time vs. CPU exec. time
  CPU exec. time equation
  CPI
  Impacting factors
  Performance evaluation tools

## Slide 4: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity

## Slide 5: Technology Trends: Microprocessor Capacity
“Moore’s Law”
2X transistors/Chip
Every 1.5 years
Who is Moore?
Trend of transistor’s size?
What is the measure of size?
Growth function?

## Slide 6: Common Terminology
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.1 The 2X vs. 10Y bytes ambiguity was resolved by adding a binary notation for all the common size terms. In the last column we note how much larger the binary term is than its corresponding decimal term, which is compounded as we head down the chart. These prefixes work for bits as well as bytes, so gigabit (Gb) is 109 bits while gibibits (Gib) is 230 bits.
Capacity of memory and disks
Speed:
KHz, MHz, GHz
KIPS, MIPS, GIPS

## Slide 7: Anatomy: 5 components of Computers
Von Neumann architectures
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
data
live when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data
live when
not running)
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 8: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 9: Inside the Processor
Apple A10 die on iphone 7

## Slide 10: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 11: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 12: Intel Core i7 Wafer
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm

## Slide 13: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 14: Defining Performance
Which airplane has the best performance?
Performance
What are the measures of processors, or computers?

## Slide 15: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 16: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B
What time are they: CPU, or + memory, or + IO?
Or what are the relative times?

## Slide 17: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 18: Summary
CPU time
Reading for next lecture
  5th ed: Chp1.6-8