## Slide 1: CPSC3300: Computer Systems Organization
Lecture 3 – Technology, Performance and Power (Continued)

## Slide 2: Administrivia
Homework 1
  Assignment description available on Canvas. Submit a word document or PDF file on Canvas.
  Use one of the school of computing Linux machines for timing experiments with the perf tool
  Figure out what commands and options of perf are needed for the experiments
  Due 11:59pm, Thursday, January 28 on Canvas
Reading sections
  Chp1.4-7; Zybooks participation activities for 1.6 – 1.7 assigned

## Slide 3: Overview
CPU performance
  Elapsed time vs. CPU exec. time
  CPU exec. time equation
  CPI
  Impacting factors
  Performance evaluation tools

## Slide 4: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance
What are the impacting factor of CPU time for my program?

## Slide 5: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period or cycle time: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (or CPU speed): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz
How many cycles/second on today’s processors?
How about a decade ago, two decades ago? What governs the speed?
What do CPUs do in a cycle?
If the CPU runs faster, how does program exec. time change?

## Slide 6: Program CPU Time
Performance improved by
  Reducing number of program clock cycles
    who can do it, software or hardware designer?
  Increasing clock rate
    who can do it, software or hardware designer?
  Hardware designer must often trade off clock rate against cycle count

## Slide 7: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 8: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI (this is true on many architectures, esp. X86)
    Average CPI affected by instruction mix

## Slide 9: CPU Performance Equation
IC
CPI
1/clock rate
Influenced by | ISA/compiler | Organization/ISA | Hardware/organization
Quantitative tools | Compiler and sw tools | Compiler and sw tools | Timing estimators
Simulators
Instrumentation
Hardware counters

## Slide 10: CPI Example
Computer A: Cycle Time = 250ps, avg. CPI = 2.0
Computer B: Cycle Time = 500ps, avg. CPI = 1.2
Same ISA, meaning the same ins. count
Which is faster, and by how much?
A is faster…
…by this much

## Slide 11: CPI in More Detail
If different instruction classes take different numbers of cycles, e.g., X86 architectures
  CPI of each class of instruction is specific and constant, determined by hardware.
  Ins. count (IC) of each class of instruction in the program can be obtained with certain tools
Weighted average CPI
Relative frequency

## Slide 12: CPI Example
Same hardware
Two code sequences generated with two compilers, both using instructions in classes A, B, C
Class | A | B | C
CPI for class, determined by hardware | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 13: Principals of Arch Design
Make common case fast (90/10 Rule)
  The most effective approach for performance improvement
Amdahl’s Law
  Law of diminishing returns
Speedup
  Achieved performance improvement over original

## Slide 14: Amdahl’s Law
Execution time of any code has two portions
Portion I: not affected by enhancement
Portion II: affected by enhancement
n is speedup factor of old/new execution times for portion II
As n -> infinity, execution timenew -> (1-) * execution timeold
 is % of original code that would benefit from enhancement
Execution timep1
Execution timep2

## Slide 15: Amdahl’s Law

## Slide 16: Example
Enhancement: Vector mode
Portions of code containing computations run 20x faster in vector mode.
What % of original code must be vectorizable to achieve speedupoverall = 2?

## Slide 17: Pitfall in Performance Evaluation
Using a subset of the performance equation as a performance metric
  Clock rate, CPI, or IC only
  Or only two of the three factors
Using million instructions per second (MIPS) as metric
  MIPS can’t be used to compare different ISAs
  MIPS varies with programs on the same computer
  MIPS can vary independently from performance

## Slide 18: Performance Summary
Performance depends on
  Algorithm: affects ?
  Programming language: affects ?
  Compiler: affects ?
  Instruction set architecture: affects ?
  IC, possibly CPI
  IC, CPI
  IC, CPI
  IC, CPI, Tc

## Slide 19: Summary
CPU time
Performance impacting factors
Reading for next lecture
  5th ed: Chp1.8-11