## Slide 1: CPSC3300: Computer Systems Organization
Lecture 4 – Benchmarking

## Slide 2: Overview
Pitfalls in performance evaluation
Power
Benchmarking
  Benchmarks
  Results analysis

## Slide 3: Performance Summary
Performance depends on
  Algorithm: affects ?
  Programming language: affects ?
  Compiler: affects ?
  Instruction set architecture: affects ?
  IC, possibly CPI
  IC, CPI
  IC, CPI
  IC, CPI, Tc
IC
CPI
Cycle time Tc
What is IPC?
What is good for your program,
a IPC high or low?

## Slide 4: Power Trends
In CMOS IC technology
The Power Wall
×1000
×30
5V → 1V

## Slide 5: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 6: Free Lunch Is Over

## Slide 7: Parallel System Are Ubiquitous Today
CMP (Chip Multiprocessing) with multiple cores
  Used in high end in servers to low power in mobiles systems
High end server processors Xeon and Opteron
  Quad-core, six-core, 10-core processors
Atom processors in netbooks
  Dual-core, quad-core, six-core
Processors in cell phones
  Dual-core, quad-core, six-core

## Slide 8: Benchmarking
Some definitions are:
It is a test that measures the performance of a system or subsystem on a well-defined task or set of task.
A method of comparing the performance of different computer architecture.
Or a method of comparing the performance of different software
Benchmarks usually report performance data

## Slide 9: Benchmarking Results Example
Compare three architectures
  Core i3-4330
  Core i3-4360
  Xeon E3-1230 V3

## Slide 10: Types of Benchmarks
Real programs.
  have input, output, and options for running the program
  E.g.: Compilers, text processing software, etc.
Kernels: small, key pieces from real programs.
  E.g.: Livermore Loops and Linpack
Toy benchmarks: typically between 10-100 lines of code
  Produce a result the user already knows
  E.g.: Sieve of Eratosthenes, Puzzle, and Quicksort
Synthetic benchmarks: to match an avg exec. profile
  Examples: Whetstone and Dhrystone.

## Slide 11: Benchmarking
Methods
  Real programs
  Modified apps (cint2000, cfp2000 of SPEC)
  Kernels
    Livermore Kernels, LinPACK
  Toy Benchmarks
    Sieve of Eratosthenes (highest common factor), quicksort
  Synthetic Benchmarks
    Whetstone, Dhrystone
Problems with benchmarking?
accuracy

## Slide 12: Benchmarking Pitfalls
Optimization option on today’s compilers can affect the results of benchmark tests
Modification of the sources (public-domain software) produces different versions of the benchmark
Many benchmarks test only one aspect of a system
  Different aspects to test are: CPU, I/O, File System, etc.
A compiler can “recognize” a benchmark suite and loads a hand-optimized algorithms for the test
Problem
  Benchmarks drive vendors to improve benchmarks

## Slide 13: Benchmark Suites
Benchmark suites
  A collection of benchmarks measuring the performance of systems/subsystems with a variety of applications.
  Weakness of any one benchmark is lessened by the presence of the other benchmarks.
  Some benchmarks are kernels, but many are real programs.
Examples
  SPEC (spec.org): cpu, cloud, storage, power…
  HPL (http://www.netlib.org/benchmark/hpl/): computer cluster
Problem
  How do we compare using a suite of applications

## Slide 14: SPEC Benchmarks Results
SPECINTC2006 benchmarks running on a 2.66 GHz Intel Core i7 920.

## Slide 15: Lies, darn lies, and statistics
To minimize
  Cheating on results
  Apples to oranges
Define methods for comparisons of workloads (benchmarks)
How to fairly compare multiple machines and codes
 | Computer 1 | Computer 2 | Computer 3
Program A | 100 | 10 | 1
Program B | 30 | 300 | 200
Total | 130 | 310 | 201
C2 is 10x faster than C1 for Prog A
C1 is 10x faster than C2 for Prog B
C3 is 10x faster than C2 for Prog A
C3 is 1.5x faster than C2 for Prog B
Using total execution time
C1 is 2.4x faster than C2
C1 is 1.5x faster than C3
C3 is 1.5x faster than C2
All quantifiable methods should be proportional to total execution time – the great comparator – ensuring reflection of real performance.

## Slide 16: Let’s get mean
Arithmetic mean
*Both track total execution time
Arithmetic mean (weighted)
201
310
130
Total
200
300
30
Program B
1
10
100
Program A
Computer 3
Computer 2
Computer 1
What about unequal emphasis of codes in suite?

## Slide 17: Weighted arithmetic mean example
 | W1=.5, W2=.5 | W1=.909,W2=.091 | W1=.999,W2=.001
Computer A | 500.5 | 91.909 | 1.999
Computer B | 55 | 18.10 | 10.09
Computer C | 20 | 20 | 20
Arithmetic mean (weighted)
 | Comp A | Comp B | Comp C
Prog 1 | 1 | 10 | 20
Prog 2 | 1000 | 100 | 20

## Slide 18: Be normal
Normalized execution time: normalize to a particular machine by dividing all execution times by chosen machine’s time
Example: Program P1 has the following execution times:
On machine A: 10 secs
On machine B: 100 secs
On machine C: 150 secs
Normalized to A: A=1, B=10, C=15
Normalized to B: A=.1, B=1, C=1.5
Execution time ratio

## Slide 19: Getting Meaner
Normalized arithmetic mean
Normalized geometric mean
 | Comp A | Comp B | Comp C
Prog 1 | 1 | 10 | 20
Prog 2 | 1000 | 100 | 20
Taking the average of the normalized times

## Slide 20: Normalized example
 | Normalized to A |  |  | Normalized to B |  |  | Normalized to C |  | 
 | A | B | C | A | B | C | A | B | C
ETR P1 | 1 | 10 | 20 | .1 | 1 | 2 | .05 | .5 | 1
ETR P2 | 1 | .1 | .02 | 10 | 1 | .2 | 50 | 5 | 1
 | Normalized to A |  |  | Normalized to B |  |  | Normalized to C |  | 
 | A | B | C | A | B | C | A | B | C
NAM | 1 | 5.05 | 10.01 | 5.05 | 1 | 1.1 | 25.0 | 2.75 | 1
NGM | 1 | 1 | .63 | 1 | 1 | .63 | 1.58 | 1.58 | 1
Bad idea

## Slide 21: Geometric vs. Arithmetic
Arithmetic mean
  Provides weighted average
  Pros: proportional to overall execution time
  Cons:
    Can be rigged easily (disproportionate problem size)
    Cannot use with normalizing
Normalized Geometric mean
  Provides relative performance of machines to ref
  Pros: same results regardless of ref machine
  Cons:
    Not proportional to overall execution time
    Large % change in small overall time contributor can skew
Suggestions
  Weight programs according to their actual frequency
  Use problem size to pre-normalize program execution time
  Combine approaches: summary of simple means and relative performance to base machine

## Slide 22: Supplemental Reading
SPEC benchmark website
  https://www.spec.org/
High performance Linpack
  http://www.netlib.org/benchmark/hpl/
High performance computing challenge
  http://icl.cs.utk.edu/hpcc/
Computer benchmarking: paths and pitfalls
  By Jack Dongarra et al

## Slide 23: Summary
CPU time calculation
Power trend and power wall
Common benchmarks
Benchmarking results analysis
Reading for next week:
  8.1-3