## Slide 1: CPSC3300: Computer Systems Organization
Lecture 5 – Combinational Logic

## Slide 2: Outline
Reading for this lecture
  8.1-3
Logic gates and functions
  Truth table
  Boolean algebra
Two-level representation (sum of product)
Example combinational logic devices
  Mux and deMux
  Adder

## Slide 3: Express Logic Function
Truth table
Boolean Algebra, named after Boole, a 19th century mathematician
  The OR operator: + or OR
  The AND operator: • or AND
  The unary operator NOT :
  The XOR operator:
  Others: NOR, NAND, XNOR
    How to express these logic functions?
+

## Slide 4: Laws of Boolean Algebra
T1 : Commutative Law
(a) A + B = B + A (b) A B = B A
T2 : Associate Law
(a) (A + B) + C = A + (B + C) (b) (A B) C = A (B C)
T3 : Distributive Law
(a) A (B + C) = A B + A C (b) A + (B C) = (A + B) (A + C)
T4 :
(a) 0 + A = A (b) 1 A = A
T5 :
(a) 1 + A = 1
(b) 0 A = 0
T6:
DeMorgan’s Theorem

## Slide 5: Switch
This circuit is built with power, switch, and wires
For the electric circuit shown by the schematic diagram
  Switch open, lamp off
  Switch close, lamp on
When the switch is closed, the path is completed, current flows, and the lamp lights.
  The voltage at position out can be 5v or 0v, depending on the state of the switch.
out
5V
Transistors are electric switches that operate fast

## Slide 6: Logic Gates
Binary numbers in computers represented with voltage ranges
    3.7v-5v: high
    0v-1.3v: low
  These two states can be reliably distinguished
Computer circuits include resistors, power, wires, and logic gates
Logic gates:
  Built of transistors
  process signals which represent true or false
  Logic states:
    True/false; 1/0; high/low; on/off
Logic gates
  Name: NOT, AND, NAND
  Symbols
  Truth table or boolean operation, expressing the function

## Slide 7: Logic Gates
Name and symbols
Why are there so many gates?
  Abstraction.
  We want our digital logic diagrams to be clear, so we want different symbols for each function.
NOT
AND
OR
NAND
XOR
NOR
XNOR

## Slide 8: The Logic Gate Game
F = ?
F =
F =

## Slide 9: Literal, Minterm, SOP
Definition:
  A variable xi has two literals: xi and xi.
  A logical product where each variable is represented by at most one literal is
    a product or
    a product term or
    a term.
  A minterm is a logical product of n literals where each variable occurs as exactly one literal
  A canonical SOP (sum-of-products) is a logical sum of minterms, where all minterms are different.

## Slide 10: Logic Functions in Two-Level Representation
SoP can be used to determine the logic functions of variables
Example: identify the function for Cout
  Given 3 variables A, B, Cin, #literals?
    6 literals: A, B, Cin, , ,
  What are the minterms with three variables?
  How to determine the function?
input |  |  | output
A | B | Cin | Cout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Minterm for each row, as if its value is 1
  1. 2. 3.
  4. 5. 6.
  7. 8.
Two level representation procedure
  Locate the entries with 1 and represent them with minterms
  Add the minterms

## Slide 11: Multiplexers
A n-1 multiplexer, or MUX, for short, is a device that allows you to pick one of n inputs and direct it to an output
Examples:
  TV: you select one of many channels to be displayed on your screen
  Radio:
An n-1 MUX consists of the following:
  Data inputs: n
  Control inputs: ceil( log2 n ) (– what is this?)
  Output: 1
Diagram of 2-1 MUX
  Data inputs: n=2 (y0, x0)
  Control inputs: ceil( log2 2 )=1;C: 1 bit
  Outputs: 1
2-1MUX
y0
x0
Z
C
x0
y0
C
Z

## Slide 12: 2-1 MUX cont’d
Behavior of 2-1 MUX
  If c==0, then x0 is directed to the output z
  If c==1, then x1 is directed to the output z
Truth table
Boolean Expression:
Implement it with logic gates by yourself
2-1MUX
x1
x0
Z
0
Row | C | X1 | X0 | Z
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 1
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
7 | 1 | 1 | 1 | 1
Row | C | Z
0 | 0 | X0
1 | 1 | X1
1

## Slide 13: Binary Addition
(0)10 = ( )2
(1)10 = ( )2
(2)10 = ( )2
(3)10 = ( )2
(4)10 = ( )2
(5)10 = ( )2
(6)10 = ( )2
(7)10 = ( )2
(8)10 = ( )2
Let's consider adding two 3-bit UB (unsigned binary) numbers.
1 1 0
+ 0 1 1
-----------

## Slide 14: Machine Addition
Consider adding two bits (binary digits) together:
A + B = ?
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
S is for “SUM”
C is for “CARRY”
C = AND(A, B)
S = XOR(A, B)
Half Adder
add two 1-digit addends, can only be
used to add the least significant bit (can’t deal
with a carry-in bit from the lower digit)

## Slide 15: Full Adder
A half Adders does not handle carries
A full adder can handle three bits
  – 3 data inputs: X, Y, and Cin
  – 2 outputs: S for sum and Cout for carry out
Truth table?
Boolean expression?
Circuits?
A | B | Cin
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Cout | S
0 | 0
0 | 1
0 | 1
1 | 0
0 | 1
1 | 0
1 | 0
1 | 1
Cout | S

## Slide 16: Summary
Truth table
Boolean algebra
Mux
Adders
Reading for next lecture
  5th ed: 8.5-6