## Slide 1: CPSC3300: Computer Systems Organization
Lecture 6 – Adders

## Slide 2: Outline
Mux
Half adder
Full adder
Carry lookahead adder
Reading
  8.5-6

## Slide 3: Multiplexers
A n-1 multiplexer, or MUX, for short, is a device that allows you to pick one of n inputs and direct it to an output
Examples:
  TV: you select one of many channels to be displayed on your screen
  Radio:
An n-1 MUX consists of the following:
  Data inputs: n
  Control inputs: ceil( log2 n ) (– what is this?)
  Output: 1
Diagram of 2-1 MUX
  Data inputs: n=2 (y0, x0)
  Control inputs: ceil( log2 2 )=1;C: 1 bit
  Outputs: 1
2-1MUX
y0
x0
Z
C
x0
y0
C
Z

## Slide 4: 2-1 MUX cont’d
Behavior of 2-1 MUX
  If c==0, then x0 is directed to the output z
  If c==1, then x1 is directed to the output z
Truth table
Boolean Expression:
Implement it with logic gates by yourself
2-1MUX
x1
x0
Z
0
Row | C | X1 | X0 | Z
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 1
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
7 | 1 | 1 | 1 | 1
Row | C | Z
0 | 0 | X0
1 | 1 | X1
1
Using 2-1 MUXes, can you build a 4-1 MUX?
Using logic gates, can you build a 1-2 deMUX?

## Slide 5: Binary Addition
(0)10 = ( )2
(1)10 = ( )2
(2)10 = ( )2
(3)10 = ( )2
(4)10 = ( )2
(5)10 = ( )2
(6)10 = ( )2
(7)10 = ( )2
(8)10 = ( )2
Let's consider adding two 3-bit UB (unsigned binary) numbers.
1 1 0
+ 0 1 1
-----------

## Slide 6: Machine Addition
Consider adding two bits (binary digits) together:
A + B = ?
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10
S is for “SUM”
C is for “CARRY”
C = AND(A, B)
S = XOR(A, B)
Half Adder
add two 1-digit addends, can only be
used to add the least significant bit (can’t deal
with a carry-in bit from the lower digit)

## Slide 7: Full Adder
A half Adders does not handle carries
A full adder can handle three bits
  – 3 data inputs: X, Y, and Cin
  – 2 outputs: S for sum and Cout for carry out
Truth table?
Boolean expression?
Circuits?
A | B | Cin
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Cout | S
0 | 0
0 | 1
0 | 1
1 | 0
0 | 1
1 | 0
1 | 0
1 | 1
Cout | S

## Slide 8: Boolean Function
Determine logic function for full adder from truth table
  C =
  S =
Add details of circuits

## Slide 9: Full Adder Implementation
Write out the logic functions for full adder
  Cout =
  S =
Add details of circuits
Build full adder with half adders and basic logic gates
Abstraction
A Full Adder

## Slide 10: Lookahead Adder
Two internal signals
  Carry propagate: if Pi=1 (Gi=0), Ci+1=Ci
  Carry generate: if G=1, Ci+1=1
  Depending on A and B only
Delay of computed values of all the Pi’s
  One XOR-gate delay after operands A and B are made valid
Delay of computed values of all the Gi’s
  One AND-gate delay after operands A and B are made valid
i

## Slide 11: Sum and Carry Based on P & G
Unroll for bit 0 to bit 4
  Values to be calculated: Si, Ci
    Use Pi and Gi, which can be calculated with one unit of delay with Ai, Bi, C0

## Slide 12: 4-bit Carry-Lookahead Adder (1)
c4 = g3 + g2 p3 + g1 p2p3 + g0p1p2p3 + c0p0p1p2p3
c3 = g2 + g1 p2 + g0 p1p2 + c0p0p1p2
c2 = g1 + g0 p1 + c0p0p1
c1 = g0 + c0 p0
s0 = a0  b0  c0 = p0  c0
s1 = p1  c1
s2 = p2  c2
s3 = p3  c3

## Slide 13: Carry Out Bit in CLA

## Slide 14: CLA Adder Implementation

## Slide 15: Three levels of Logic in CLA
1st level
  Generate all the P & G signals with XOR gates and AND gates
    P & G valid after 1 unit of time (one gate)
2nd level
  2-level implementation logic circuit
    First: AND gate
    Second: OR gate
  Signals C be valid after 2 + 1 units of time
3rd level
  XOR gates generate signal S
  Signal S be valid after 1 + 2 + 1 units of time
How many time units does a 4-bit ripple adder take?

## Slide 16: Summary
Mux and deMux
Half adder
Full adder
Carry look ahead adder
Next lecture reading
  5th ed: 8.7-8