## Slide 1: CPSC3300: Computer Systems Organization
Lecture 7 – Sequential Logic

## Slide 2: Administrivia
Exam 1
  Thursday 2/11
  Covers material introduced by Tuesday 2/9 (Lecture 8 - Example Devices and Finite State Machines)
  Readings, homework assignments, textbook, slides
Homework 2 (Boolean Algebra & Adders) available
  Due Monday 2/8 at 11:59pm
Today
  Sequential logic and devices
  Reading: 8.7-8

## Slide 3: ALU
ALU
  Arithmetic Logic Unit
    Arithmetic operations: +, -, *, /, %
    Logic operations: AND, OR, NOT, XOR
The 1-bit logical unit for AND and OR
The 1-bit ALU for AND, OR, and addition

## Slide 4: 1-bit ALU
Support on (a, b), (a, not b)
  AND
  OR
  Addition
Support on (a, b), (a, not b), (not a, b), (not a, not b)
  AND
  OR
  Addition

## Slide 5: ALU

## Slide 6: Combinational Logic Circuits
So far, we learned about combination logic
Combinational logic circuits
  Have inputs and outputs
  Implement Boolean functions and mathematical operations
  Output depends only on present inputs.
  Example:
    Input 000  combinational logic circuits  100 (fixed mapping)

## Slide 7: What is State?
Mathematical functions are stateless
  take inputs, and produce the corresponding outputs.
  do not store information or data
Definition of state:
  State is a quantity that stores the previous history of what's happened in such a way that you can predict the output, given any future input.

## Slide 8: Sequential Logic Circuits
Sequential logic circuits
  Contains one or more combinational logic blocks
  Have state in a feedback loop with the logic
  use a clock.
  The next state depends on the inputs and the present state
  The output depends on the present state and perhaps also the inputs
Sequential logic circuits have memory

## Slide 9: A Basic Two-Inverter Element
A memory cell:
  Two inverters connected back-to-back, i.e. output of one to input of the other and vice-versa.
Using feedback to store the value or hold the value.
Two stable states
  V01 = 0 and V02 =1
  V01 = 1 and V02 = 0
v01
v02
v01
v02

## Slide 10: Clock and Clock Edges
Timing diagram is used to describe the behavior of a clock
Very small transition time: 0 -> 1 and 1 -> 0.
  Positive edges: the clock transitions from 0 to 1
  Negative edges: the clock transitions from 1 to 0
Why are clock edges important
  Flip flops and registers are timed devices and triggered by edges.
  Why flip flops are built this way?
exaggerated transitions
Time on X, voltage on y

## Slide 11: SR Latch
The NOR-based SR Latch
  contains the basic memory cell to allow setting the state of the latch.
  Inputs: S (set) and R (reset)
  Outputs: Q and Not Q
;
Behavior:
  When S=0 and R=0, feedback loop maintains state.
    If =0, =0; If =1, =1
  When S=1 and R=0, Q is set to 1.
  When S=0 and R=1, Q is reset to 0
  (S=1 and R=1) is not allowed
  Set line latches a 1.
  Reset line resets or clears latch.

## Slide 12: Clocked SR Latch
The NOR-based SR latch with a clock added.
  The latch is responsive to inputs S and R only when CLK is high (level)
  When CLK is low, the latch retains its current state
Timing diagram shows the level-sensitive nature of the clocked SR latch.
  Note four times where Q changes state:
    When S goes high during positive CLK
    On leading CLK edge after changes in S & R during CLK low time
    A positive glitch in S while CLK is high
    When R goes high during positive CLK
S
R
Q
Q
CLK

## Slide 13: D Latch
Data latch, simply D Latch
A D-latch is implemented with
  a clocked, NOR-based S-R latch
  D connected to S
  Inverted D connected to input R
Behavior
  When CLK is high, D is transmitted to output Q (and D’ to Q’)
  When CLK is low, the latch retains its previous state
Transparent latches are typically used as I/O ports or in asynchronous systems, or in synchronous two-phase systems

## Slide 14: Edge-Triggered D Flip-Flops
Synchronous sequential circuits –inputs captured at only discrete instants of time, such as the rising edges of the clock.
Latches are level-triggered, not practical for use in synchronous sequential circuits.
Behavior:
  Rising edge: sample input D and direct it to Qnext
    If D=0 then Qnext=0; if D=1 then Qnext=1
  Non-rising edge, Qnext=Q, no matter what value input D is.
A D flip-flop can be viewed as a memory cell.
Positive Edge Triggered D Flip-Flops

## Slide 15: Register File
Register file: a set of registers that can be read and written by supplying a register number to be accessed

## Slide 16
16
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE B.8.8 The implementation of two read ports for a register file with n registers can be done with a pair of n-to-1 multiplexors, each 32 bits wide. The register read number signal is used as the multiplexor selector signal. Figure B.8.9 shows how the write port is implemented.

## Slide 17
17
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE B.8.9 The write port for a register file is implemented with a decoder that is used with the write signal to generate the C input to the registers. All three inputs (the register number, the data, and the write signal) will have setup and hold-time constraints that ensure that the correct data is written into the register file.

## Slide 18: Administrivia
Exam 1
  Online via Canvas
  Exam is open-notes
  Thursday February 11
  HW1 solution will be available on Canvas, HW2 questions will be explained during the review session before the exam
  Sample questions will be available on Canvas

## Slide 19: Summary
Difference between combinational and sequential logics
ALU
Feedback circuits
Latches
Flip-flops
Reading for next lecture
  8.10