## Slide 1: CPSC3300: Computer Systems Organization
Lecture 8 – Counters and Finite State Machines

## Slide 2: Administrivia
Exam 1
  Online via Canvas
  Exam is open-notes
  Thursday February 11
  Sample questions will be available on Canvas

## Slide 3: Overview
A sequential device: counters
Finite state machines

## Slide 4: Sequential logic implementation
Models for representing sequential circuits
  finite-state machines (Moore and Mealy)
  representation of memory (states)
  changes in state (transitions)
Basic sequential device
  counters

## Slide 5: State Machine Model
States: S1, S2, ..., Sk
Inputs: I1, I2, ..., Im
Outputs: O1, O2, ..., On
Transition function: Fs(Si, Ij)
Output function: Fo(Si) or Fo(Si, Ij)

## Slide 6: FSM design procedure
Describe FSM behavior, e.g. state diagram
  Inputs and Outputs
  States (symbolic)
  State transitions
State diagram to state transition table
  Inputs: inputs and current state
  Outputs: outputs and next state
Implementation
  flip-flop for each state bit
  synthesize combinational logic from encoded state table

## Slide 7: Counters
A0
A1
A2
A3
This counter counts from 0000, 0001, 0010, …, to 1110, 1111, 0000 cycle by cycle and restarts.

## Slide 8: Example: Implement a Modulo-4 Synchronous Counter
Using D Flip-Flops
Counts from 0 to 3 and then repeats.
It has a clock input (CLK) and a RESET input.
Outputs appear as a sequence of values (q1 and q0) at time steps corresponding to the clock.
As the outputs are generated, a new state (s1s0) is generated and fed back to the D flip-flops.

## Slide 9: The Mod-4 Counter
Requires four states, encoded in binary, with at least two bits for them to be encoded uniquely.
  A = 00
  B = 01
  C = 10
  D = 11
The input requires only a single bit.
  0 | 1

## Slide 10: State Transition Diagram for the Mod-4 Counter

## Slide 11: State Encoding and Table
Next state
Output
In this example, output happens to be the same as the next state. They are usually
different for most devices.

## Slide 12: State Table for the Mod-4 Counter

## Slide 13: Logic Design for Mod-4 Counter

## Slide 14: Summary
Counter
  An important device on processors
Finite state machine for sequential circuit
  State diagram
  State transition table
  Circuit design